## Slide 1: Format and Contents of Safety Analysis Report
Yong Ho RYU, Ph.D.
Korea Institute of Nuclear Safety
Notes: 목표
  많은 연구와 이론, 실효성 위주 접근을 추진
  문화와 안전문화를 이해
  IAEA를 비롯한 국제사회의 동향을 파악
  안전문화 조성 및 증진을 위한 2개 관점을 이해
    조직 차원의 조치사항
    개인의 역할

## Slide 2: Table of Contents
Introduction
Available Formats : IAEA GS-G-4.1 and USNRC RG 1.70
Comparison of Individual Chapters
Chapter on Safety Analyses
Formal Aspects
Remarks
Appendix 1. Contents of SAR (IAEA GS-G-4.1)

## Slide 3: I. Introduction
Demonstration of safety for the authorization (GSR Part 1, Requirement 24: )
  Authorization stages in the lifetime include:
Site evaluation, design, construction, commissioning, operation, shutdown and decommissioning
Management of radioactive waste and the management of spent fuel
  Prior to granting of an authorization, the applicant shall submit a safety assessment associated with facilities and activities.
  The regulatory body shall issue guidance on format and content of the documents to be submitted by the applicant for an authorization.

## Slide 4: I. Introduction
Review and assessment of information relevant to safety (GSR Part 1, Requirement 25)
  The regulatory body shall review and assess relevant information to determine whether facilities and activities comply with regulatory requirements.
  Technical and other documents submitted by the applicant shall be reviewed and assessed by regulatory body.
  The regulatory body shall asses all radiation risks associated with facilities and activities.

## Slide 5: I. Introduction
Results of Review & Assessment by Regulator
Contents of documentation for the results of review & assessment
Basis for the evaluation & the evaluation results
Independent analysis performed by regulatory staff
Comparison with similar (reference) facilities
Conformance with regulatory requirements & guides
Conclusions & reasons for the decisions on license
Any additional conditions to be fulfilled by operator

## Slide 6: I. Introduction
The purpose of SAR:
  an important part of the licensing basis
  reference material for the safe operation of the plant
The SAR is the basic reference material of the plant:
  The SAR should present sufficient information on the plant that, for the purposes of nuclear and radiation safety assessment.
  The SAR may refer to more detailed supplementary information (which should be however available for the review on request).

## Slide 7: I. Introduction
GSR-part 4 on Documentation of Safety Assessment
  4.62. SAR: demonstrating that the facility or activity is in compliance with the fundamental safety principles, this Safety Requirements, and any national laws and regulations
  4.63. The quantitative and qualitative outcomes of the safety assessment form the basis for the safety report, supplemented by supporting evidence for and reasoning about the robustness and reliability of the safety assessment and its assumptions, including information on the performance of individual components of systems as appropriate.
  4.64. The safety report has to document the safety assessment in sufficient scope and detail to support the conclusions reached and to provide an adequate input into independent verification and regulatory review. The safety report includes:
    A justification for the selection of the anticipated operational occurrences and accidents considered in the analysis;
    An overview and necessary details of the collection of data, the modelling, the computer codes and the assumptions made;
    Criteria used for the evaluation of the modelling results;
    Results of the analysis covering the performance of the facility or activity, the radiation risks incurred and a discussion of the underlying uncertainties;
    Conclusions on the acceptability of the level of safety achieved and the identification of necessary improvements and additional measures.
  4.65. The safety report is to be updated as necessary.

## Slide 8: II. Available Formats
Typically, the national legislation prescribes some form for the SAR, which is based either on the RG 1.70 or on the GS-G-4.1.
  Regulatory Guide 1.70 (Revision 3), Standard Format and Content of Safety Analysis Reports for Nuclear Power Plants, LWR Edition (first issued 1972, latest revision 1978)
    Download: https://www.nrc.gov/docs/ML011340122.html
    This is the most widely accepted and applied format and most detailed description of the contents (400 pages)
  Format and Content of the Safety Analysis Report for Nuclear Power Plants, IAEA, GS-G-4.1 (2004)
    Download: http://www-pub.iaea.org/MTCD/publications/PDF/Pub1185_web.pdf
    This guide represents the minimum requirements about the SAR, as accepted by all IAEA member states (79 pages).

## Slide 9: Comparison of the formats
RG-1. 70 (US-NRC) | GS-G-4.1 (IAEA)
1. Introduction and general description of the plant | 1. Introduction
2. Site Characteristics | 2. General Plant Description
3. Design of Structures, Components, Equipment and Systems | 3. Management of Safety
4. Reactor | 4. Site Evaluation
5. RCS and Connected Systems | 5. General Design Aspects
6. Engineered Safety Features | 6. Description and conformance to the design of plant systems
7. Instrumentation and Controls | 7. Safety analyses
8. Electric Power | 8. Commissioning
9. Auxiliary Systems | 9. Operational aspects
10. Steam and Power Conversion | 10. Operational limits and conditions
11. Radioactive Waste Management | 11. Radiation protection
12. Radiation Protection | 12. Emergency preparedness
13. Conduct of Operations | 13. Environmental aspects
14. Initial Test Program | 14. Radioactive waste management
15. Accident Analyses | 15. Decommissioning and end of life aspects
16. Technical Specifications | The NRC guide is more detailed, the IAEA guide is more up-to-date
17. Quality Assurance | 

## Slide 10: II. Available Formats
  New aspects addressed in the IAEA GS-G-4.1 compared with original RG 1.70
    Defence in depth principles (not systematically described in RG 1.70)
    Management of safety, including safety culture
    More details on operational aspects
    Decommissioning phase of NPPs
    Environmental aspects
    Emergency preparedness
    Analysis of beyond design basis accidents and severe accidents
    Probabilistic Safety Analysis
    Different structure of safety report
    All safety analyses (from normal operation up to severe accidents, TH, PTS, containment, radiological aspects) presented in one chapter
  The environmental aspects are often taken care of in a separate document in RG 1.70.

## Slide 11: II. Available Formats
Updates of RG 1.70
Regulatory Guide 1.206 - Combined License Applications for Nuclear Power Plants, June 2007, applicable for new LWRs
RG 1.206 includes two additional chapters
  18. Human Factors Engineering; it shall be demonstrated that acceptable HFE practices and guidelines are incorporated into the plant’s design.
  19. Probabilistic Risk Assessment and Severe Accidents; contains summary of design-specific or plant-specific PRA as well as deterministic evaluation of design features for the prevention or mitigation of severe accidents.
Detailed contents of the SAR can be verified for all chapters, including 18 and 19, using US NRC Standard Review Plan, NUREG 0800, Rev.2, June 2007.

## Slide 12: Example of RG 1.70 applications
AP-1000 (UK) | APR-1400 (ROK)
1. Introduction and General Description of the Plant | 1. Introduction and General Description of Plant
2. Site Characteristics | 2. Site Envelope Characteristics
3. Design of Structures, Components, Equipment and Systems | 3. Design of Structures, Components, Equipment and Systems
4. Reactor | 4. Reactor
5. RCS and Connected Systems | 5. RCS and Connected Systems
6. Engineered Safety Features | 6. Engineered Safety Features
7. Instrumentation and Control | 7. Instrument and Controls
8. Electric Power | 8. Electric Power
9. Auxiliary Systems | 9. Auxiliary Systems
10. Steam and Power Conversion | 10. Steam and Power Conversion System
11. Radioactive Waste Management | 11. Radioactive Waste Management
12. Radiation Protection | 12. Radiation Protection
13. Conduct of Operations | 13. Conduct of Operations
14. Initial Test Program | 14. Initial Test Program
15. Accident Analyses | 15. Accident Analyses
16. Technical Specifications | 16. Technical Specifications
17. Quality Assurance | 17. Quality Assurance Program
18. Human Factors Engineering | 18. Human Factors Engineering
19. Probabilistic Risk Assessment and Severe Accidents | 19. Probabilistic Safety Assessment and Severe Accident Analysis
20. Decommissioning | 
21. Construction Verification Process | 
APR-1400 SAR corresponds to the updated RG 1.70

## Slide 13: III. Comparison of Individual Chapters
Ch.3. Management of Safety, IAEA GS-G-4.1 | Ch.17, Quality Assurance, RG 1.70
3.1 General considerations | 17.1 Quality Assurance During Design and Construction
3.2 Specific aspects of the management processes | 17.1.1 Organization
3.2.1 Statement of safety policy (including standards, resources and targets) | 17.1.2 Quality Assurance Program
3.2.2 Management structures, responsibilities and accountabilities | 17.1.3 Design Control
3.2.3 Planning (including risk assessment) | 17.1.4 Procurement Document Control
3.2.4 Control of safety related activities | 17.1.5 Instructions, Procedures, and Drawings
3.2.5 Ensuring competence | 17.1.6 Document Control
3.2.6 Communication and team support | 17.1.7 Control of Purchased Equipment, and Services
3.2.7 Supervision | 17.1.8 Identification/Control of Materials and Components
3.2.8 Measuring performance | 17.1.9 Control of Special Processes
3.2.9 Audit and review | 17.1.10 Inspection
3.2.10 Corrective action and improvements | 17.1.11 Test Control
3.3 Monitoring and review of safety performance | 17.1.12 Control of Measuring and Test Equipment
3.4 Consideration of Safety Culture | 17.1.13 Handling, Storage, and Shipping
3.5 Quality Assurance | 17.1.14 Inspection, Test, and Operating Status
3.5.1 QA system of the owner | 17.1.15 Nonconforming Materials, Parts, or Components
3.5.2 QA system of the contractor | 17.1.16 Corrective Action
3.5.3 QA system of the operating organization | 17.1.17 Quality Assurance Records
The “Management of Safety” incorporates the QA and also all safety specific aspects of the management; the arrangements to enhance the “Safety Culture” | 17.1.18 Audits
 | 17.2 Quality Assurance During the Operations Phase

## Slide 14: III. Comparison of Individual Chapters
Ch.5. General Design Aspects, IAEA GS-G-4.1 | Ch.3, Design of Structures, Components, Equipment, and Systems, RG 1.70
5.1 GENERAL CONSIDERATIONS | 3.1 Conformance with NRC General Design Criteria
5.2 SAFETY OBJECTIVES AND DESIGN PRINCIPLES | 3.2 Classification of Structures, Components, and Systems
5.2.1 Defence in depth | 3.3 Wind and Tornado Loadings
5.2.2 Safety functions | 3.4 Water Level (Flood) Design
5.2.3 Deterministic principles and design criteria | 3.5 Missile Protection
5.2.4 Single Failure criterion | 3.6 Protection against Dynamic Effects associated with Piping
5.2.5 Probabilistic quantitative design targets | 3.7 Seismic Design
5.2.6 Radiation protection targets and criteria | 3.8 Design of Category I Structures
5.3 CONFORMANCE WITH DESIGN PRINCIPLES/CRITERIA | 3.9 Mechanical Systems and Components
5.4 CLASSIFICATION OF SSCs | 3.10 Seismic Qualification of Seismic Category I I&C
5.4.1 Approach to safety classifications of SSCs | 3.11 Environmental Design of Mechanical and Electrical Equipment
5.5 CIVIL ENGENEERING WORKS AND STRUCTURES | 
5.5.1 Building Design Principles and Criteria | 
5.5.2 Structure and Building Loads | 
5.5.4 Seismic classification of buildings and structures | 
5.6 SYSTEM QUALIFICATION AND ENVIRONMENT FACTORS | 
5.6.1 Description of the qualification procedure for systems | 
5.6.2 Seismic qualification | 
5.6.3 Environmental qualification | 
5.6.4 EMC Qualification | 
5.7 HUMAN FACTOR ENGENEERING | 
5.8 INTERNAL AND EXTERNAL RISK | 
5.8.1 Protection against External Natural Hazards | 
5.8.2 Protection against man-made external hazards | 
5.8.3 Protection against internal hazards | 

## Slide 15: III. Comparison of Individual Chapters
Ch. 9, Operational aspects, IAEA GS-G-4.1 | Ch.13, Conduct of operations, RG 1.70
Organization – administrative procedures | Operating Organization Management and Technical Support Organization Administrative Procedures - General Administrative Procedures - Initial Test Program
Operating procedures (incl. EOPs and SAMG) | Operating and Emergency Operating Procedures
Maintenance, surveillance, inspection and testing procedures | Maintenance and Other Operating Procedures
Core management and fuel handling (incl. spent fuel) | ______
Ageing management | ______
Modifications control | ______
Qualification and training of personnel – Human factors | Reactor Operator Re-qualification Program; Reactor Operator Training Non-Licensed Plant Staff Training
Operational experience feedback program | ______
Documents and records | ______
Outage arrangements | ______
____________ | Emergency Planning Physical Security Operational Programs

## Slide 16: III. Comparison of Individual Chapters
Ch.8. Commissioning, IAEA GS-G-4.1 | Ch.14, Initial Test Program, RG 1.70
8.1 Regulatory/NPP Documents Required for Commissioning | 14.1 Specific Information To Be Included in Preliminary SAR
8.2 Commissioning Organization | 14.1.1 Scope of Test Program
8.3 Nuclear Power Plant Commissioning Stages | 14.1.2 Plant Design Features That Are Special or Unique
8.3.1 List of Stages of NPP Commissioning | 14.1.3 Regulatory Guides
8.3.2 Brief Description of NPP Commissioning Stages | 14.1.4 Utilization of Plant Operating and Testing Experiences at Other Reactor Facilities
8.4 Cooperation during Commissioning | 14.1.5 Test Program Schedule
8.4.1 Main Participants to Cooperation in Commissioning | 14.1.6 Trial Use of Plant Operating and Emergency Procedures
8.4.2 Main Areas of Cooperation in Commissioning | 14.1.7 Augmenting Applicant's Staff During Test Program
8.4.3 Assumed Basic Principles of Cooperation | 14.1.8 NSSS Interface
 | 14.1.8 BOP Interface
 | 14.2 Specific Information To Be Included in Final SAR
 | 14.2.1 Summary of Test Program and Objectives
 | 14.2.2 Organization and Staffing
 | 14.2.3 Test Procedures
 | 14.2.4 Conduct of Test Program
 | 14.2.5 Review, Evaluation, and Approval of Test Results
 | 14.2.6 Test Records
 | 14.2.7 Conformance of Test Programs with Regulatory Guides
 | 14.2.8 Utilization of Reactor Operating and Testing Experiences in Development of Test Program
 | 14.2.9 Trial Use of Plant Operating and Emergency Procedures
 | 14.2.10 Initial Fuel Loading and Initial Criticality
 | 14.2.11 Test Program Schedule
 | 14.2.12 Individual Test Descriptions

## Slide 17: III. Comparison of Individual Chapters
Ch.15, Decommissioning and End of Life Aspects, IAEA GS-G-4.1 | Ch.20, Decommissioning, RG 1.70
15.1 General Considerations | 20.1 Introduction
15.1.1 Decommissioning Strategy | 20.2 Assumptions
15.2 Decommissioning Concept | 20.3 Decommissioning Stages
15.2.1 Defining Conditions and Input Data | 20.3.1 Stage 1 Decommissioning
15.2.2 Radiation Situation at the Shutdown Point | 20.3.2 Stage 2 Decommissioning
15.2.3 Variant 1 - Immediate removal | 20.3.3 Stage 3 Decommissioning
15.2.4 Variant 2 - Removal after safe closure | 20.4 Decommissioning Strategies
15.2.5 Comparison of the two variants of decommissioning | 20.4.1 Immediate Dismantling
15.2.6 Radwaste management | 20.4.2 Deferred Dismantling (or Safe Enclosure)
15.3 Provisions for Safety During Decommissioning | 20.4.3 Entombment
15.3.1 Radiation protection | 20.4.4 Variations
15.3.2 Environmental and population impact | 20.5 Objectives
15.3.3 Radiological hazards during the decommissioning | 20.5.1 Regulatory and Licensing Guidelines
15.4 Comparison of Different Approaches to Decommissioning | 20.5.2 Sources of Radioactivity
15.5 Planning of the Preliminary Work | 20.5.3 AP1000 Design Features to Minimize Radioactive Waste
 | 20.5.4 Decommissioning Cost

## Slide 18: IV. Chapter on Safety Analyses
From safety analysis point of view, the central chapter is Ch. 7 in GS-G-4.1 (or Ch. 15 in RG 1.70), as the SAR stands for Safety Analysis Report.
Ch. 7 of the SAR is closely related to several other chapters, e.g.:
  Chapters 5-6 – without the knowledge of plant systems, it can not be judged whether the assumptions in the safety analyses are adequate and/or conservative.
  Chapter 10 – the knowledge of the OLC (Operational limits and conditions) is necessary to judge the proper selection of initial conditions in the analyses.
  To review the assumed hazards, the knowledge of other chapters is also necessary (e. g. Site specification).
Notes: 18

## Slide 19: IV. Chapter on Safety Analyses
The analyses shall include the normal operation, the anticipated operational occurrences, the design basis accidents.
The analyses should also include the PSA studies (Levels not specified), design extension conditions including selected severe accidents.
It is stated that “The analyses typically focus on neutronics and thermal-hydraulic, structural and radiological aspects…”, but no clear statement that all aspects should be analysed in this chapter.
Additional guidance : Safety Assessment for Facilities and Activities No. GSR Part 4 (Rev.1).

## Slide 20: IV. Chapter on Safety Analyses
Distribution of safety analyses in various parts of SAR according to RG 1.70
    Chapter 3: External hazards
    Chapter 5: Pressurized thermal shock
    Chapter 6:
        Containment pressure response for various LOCAs
        Analysis of passive core cooling in case for various transients and accidents
        Releases and distribution of fission products in the containment
    Chapter 11: Releases from the radwaste treatment systems up to the level of doses
    Chapter 12: Estimation of on-site and off-site doses during normal operation
    Chapter 15: Design basis accidents, including ATWS and radiological effects
    Chapter 19:
        PSA
        severe accident phenomena
        hydrogen generation and mixing
        low power and shutdown PRA analysis
        internal hazards analysis
        deterministic analysis of accidents occurring at shutdown operational modes including radiological consequences (in appendix to Chapter 19)
Notes: 20

## Slide 21: Structure of the Safety Analysis Chapter based on RG 1.70
Chapters 15 and 19, AP-1000, UK
Chapter 15. Accident analysis
15.0. General introduction to accident analysis (plant characteristics, systems and components available, FP inventories, computer codes used, component failures, operator actions, LOOP)
15.1 Increase in Heat Removal From the Primary System – includes radiological consequences
15.2 Decrease in Heat Removal by the Secondary System
15.3 Decrease in Reactor Coolant System Flow Rate – includes radiological consequences
15.4 Reactivity and Power Distribution Anomalies – includes radiological consequences
15.5 Increase in Reactor Coolant Inventory
15.6 Decrease in Reactor Coolant Inventory (LOCA, PRISE,...)– includes radiological consequences
15.7Radioactive Release from a Subsystem/Component (radwaste leakages, fuel handling accidents)
15.8 Anticipated Transients Without Scram
Appendix 15A. Evaluation Models and Parameters for Analysis of Radiological Consequences of Accidents – includes off-site doses, MCR doses
Appendix 15B. Removal of Airborne Activity from the Containment Atmosphere following a LOCA
CHAPTER 19 Probabilistic Risk Assessment
Subchapters 19.1 through 19.59 : all details about PSA modelling and results
Appendix 19A. Thermal-Hydraulic Analysis to Support Success Criteria
Appendix 19B. Ex-vessel Severe Accident Phenomena
Appendix 19C. Additional Assessment of AP1000 Design Features
Appendix 19D. Equipment Survivability Assessment
Appendix 19E. Shutdown Evaluation (systems needed, maintenance guidelines, deterministic analysis, technical specifications, shutdown risk evaluation)

## Slide 22: IV. Chapter on Safety Analyses
Comparison of requirements on PSA (PRA)
  Requirements on covering PSA (PRA) in USNRC RG and IAEA GS are similar: a description of the PRA and its results, focused on a qualitative description of insights and uses, as well as some quantitative PRA results, so that it is demonstrated that risk insights were factored into the design. The complete PSA (e.g., models, analyses, data, and codes) shall be available for an audit.
  Results of PSA (PRA) may be compared with probabilistic safety goals (neither IAEA nor NRC consider quantitative numbers as requirements): NRC specifies less than 1x10-4/year for CDF and less than 1x10-6/year for LRF, IAEA at Safety Guide level considers for new reactors 1x10-5/year for CDF and less than 1x10-6/year for LRF.

## Slide 23: IV. Chapter on Safety Analyses
Comparison of guidance on severe accidents
  For severe accidents, NRC specifies containment performance goal, which includes (1) a deterministic goal that containment integrity be maintained for approximately 24 hours following the onset of core damage for the more likely severe accident challenges and (2) a probabilistic goal that the conditional containment failure probability be less than approximately 0.1 for the composite of all core damage sequences assessed in the PRA. SAR shall demonstrate the design’s robustness, levels of defense-in-depth, and tolerance of severe accidents initiated by either internal or external events. This demonstration shall assess severe accident prevention and mitigation features, considering all relevant phenomena and vulnerability of the plant to this phenomena.

## Slide 24: IV. Chapter on Safety Analyses
Comparison of guidance on severe accidents (cont’d)
  GS-G-4.1 considers severe accidents and PSA as consistent part of safety analysis to be done for all plant states. Similarly as in RG 1.70 it is required to identify accidents leading to significant core damage and off-site releases. It is further required to perform detailed analysis needed for development of AMP and emergency preparedness planning.
  In some countries there are radiological criteria in terms of doses specified for the most exposed individual. This seems to be in compliance with the IAEA Safety Standards. GS-G-4.1 recognizes the use of severe accident analysis results for emergency preparedness and also for habitability of the control room. These can be interpreted as requirement to perform analysis of severe accidents up to the doses. However, neither GS-G4.1 nor 1.70 is completely clear on that.

## Slide 25: V: Formal aspects
User friendly format :
    At present the SAR should be available in electronic form to enhance its use and review.
    In electronic form the internal reference links are very useful.
    Though the IAEA guide only encourages the external references, their extended use is almost inevitable (detailed design documents, references to standards, detailed safety analysis reports, etc.).
    References to lower level documents are also useful (e. g. operational and emergency procedures).

## Slide 26: V: Formal aspects
Depth of description :
  It is basically determined by the requirement that the SAR is a reference material, thus the report shall be understandable by itself.
  Since it is the most detailed safety document, every safety related aspect shall be described, e.g.:
    External hazards
    Internal hazards
    Engineered safety features
    Operational arrangements
    Maintenance aspects
    Clear boundaries of the design basis etc.

## Slide 27: V. Formal aspects
Supporting materials
  The most important supporting materials, drawings, safety analysis reports, code validation reports, source material for PSA input data, etc. should be supplemented to the SAR. These materials are enhancing the review process and the later usability of the SAR.
  Some, less essential external references are usually not submitted together with the SAR to the Regulator, but they should be made available on request.

## Slide 28: VI. Remarks
There are two formats available to be followed: RG 1.70 with updates, and IAEA GS-G-4.1.
NRC guide is more detailed, IAEA guide is more up-to-date and in general terms more comprehensive.
The vendors of new reactors still follow RG 1.70.
Unified format preferred: broader consensus needed for future; RG 1.70 has better chance to succeed, with modifications using IAEA GS-G-4.1.
Design extension conditions including severe accidents should be covered by the safety analysis report as all plant states: dedicated systems for mitigation of severe accidents to be described together with other safety systems and analysis of severe accidents to be included in the chapter on safety analysis.
Current SAR formats developed by the major vendors should be taken into account.

## Slide 29: Appendix 1. Contents of SAR(GS-G-4.1)
Chapter of SAR (GS-G-4.1)
  Chapter I: Introduction
  Chapter II: General plant description
  Chapter III: Management of safety
  Chapter IV: Site evaluation
  Chapter V: General design aspects
  Chapter VI: Description & conformance to the design of plant systems
  Chapter VII: Safety analyses
  Chapter VIII: Commissioning
  Chapter IX: Operational aspects
  Chapter X: Operational limits & conditions
  Chapter XI: Radiation protection
  Chapter XII: Emergency preparedness
  Chapter XIII: Environmental aspects
  Chapter XIV: Radioactive waste management
  Chapter XV: Decommissioning & end of life aspects

## Slide 30: Appendix 1. (continued)
Chapter I: Introduction
  General Consideration
- The main purpose of the SAR
- The existing authorization status
- An identification of the designer, vendor, constructor and operating organization of the NPP
- Any similar (or identical) NPPs already reviewed and approved and a statement of the specific differences and improvements
- The main information on the preparation of the SAR;
- A description of the structure of the SAR

## Slide 31: Appendix 1. (continued)
Chapter II: General Plant Description
  Applicable regulations, codes and standards
Basic technical characteristics
Chapter II: General Plant Description
  Information on Layout and other Aspect
Operating Modes of NPP
Material incorporated by Reference
Chapter III: Management of Safety
  Consideration of Safety Culture
Quality Assurance (QA)
Monitoring and Review of Safety Performance

## Slide 32
Chapter IV: Site Evaluation
  Site Reference Data
  Evaluation of Site Specific Hazards
  Proximity of Industrial, Transport and Military Facilities
  Activities at the Plant Site
  Hydrology, Meteorology and Seismology
  Radiological Conditions due to External Sources
  Site Related Issues in Emergency Planning and Accident Management
  Monitoring of Site Related Parameters
Appendix 1. (continued)

## Slide 33: Appendix 1. (continued)
Chapter V: General Design Aspect
  Safety Objectives and Design Principles
  Conformance with the Design Principles and Criteria
  Classification of SSCs
  Civil Engineering Works and Structures
  Equipment Qualification and Environmental Factors
  Human Factors Engineering
  Protection against Internal and External Hazards

## Slide 34: Appendix 1. (continued)
Chapter VI: Description and Conformance to the Design of Plant System
  General Considerations depend on Type and Design of Reactor
  Reactor
  Reactor Coolant and Associated Systems
  Engineered Safety Features
  Instrumentation and Control
  Plant Auxiliary Systems
  Power Conversion Systems
  Radioactive Waste Treatment Systems
  Fuel Handling and Storage Systems
  Radioactive Waste Treatment Systems

## Slide 35: Appendix 1. (continued)
Chapter VII: Safety Analysis
  Safety Objective and Acceptance Criteria
  Identification and Classification of PIEs
  Human Actions
  Deterministic Analysis
  Probabilistic Analysis
  Summary of Results of the Safety Analysis
Chapter VIII: Commissioning
  General Consideration

## Slide 36: Appendix 1. (continued)
Chapter IX: Operational Aspects
  Organization
  Administrative Procedure
  Operating Procedures
  Emergency Operating Procedures
  Guidelines for Accident Management
  Maintenance, Surveillance, Inspection and Testing
  Core Management and Fuel Handling
  Management of Aging
  Control of Modification

## Slide 37: Appendix 1. (continued)
Chapter IX: Operational Aspects
  Qualification and Training of Personnel
  Human Factors
  Program for the Feedback of Operational Experience
  Documents and Records Control
  Outage
Chapter X: Operational Limits and Conditions
  General Consideration

## Slide 38: Appendix 1. (continued)
Chapter XI: Radiation Protection
  Application of the ALARA Principle
  Radiation Sources
  Design Features for Radiation Protection
  Radiation Monitoring
  Radiation Protection Program
Chapter XII: Emergency Preparedness
  General Consideration
  Emergency Management
  Emergency Response Facilities
  Capability for Assessment of Accident Progression, Radioactive Release and Consequences

## Slide 39: Appendix 1. (continued)
Chapter XIII: Environmental Aspects
  Radiological Impacts
  Non-radiological Impacts
Chapter XIV: Radioactive Waste Management
  Control of Waste
  Handling of Waste
  Minimizing the Accumulation of Waste
  Conditioning of Waste
  Storage of Waste
  Disposal of Waste

## Slide 40: Appendix 1. (continued)
Chapter XV: Decommissioning and End of Life Aspects
  Decommissioning Concept
  Provisions for Safety during Decommissioning
  Differing Approaches to Dedommissioning
  Planning of the Preliminary Work

## Slide 41
Always we keep watching
our Atomic Power